## Slide 1
Hybrid Safety Solutions Presentation
Chris Brogli - Ross Controls
Global VP of Safety Business Development Manager
chris.brogli@rosscontrols.com
1-859-595-9630
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 2: Hybrid Safety Solutions include electrical, electronic and fluid power solutions.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Input/Triggering Device
Logic Device
Output Device
Complete Safety Function
+
+
=
Hybrid safety solutions use a combination of electrical, electronic and electro-mechanical devices to control the sources of hazardous energy.

## Slide 3: Determination of the type of safety devices should be determined thru the use of a risk assessment.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Lockout/Tagout
Risk Assessment
Electrical
Fluid Power
Holistic risk assessments consider all sources of hazardous energy and includes lock-out/tag-out.

## Slide 4: Most of the identified risk reduction measures are similar in electrical and fluid power.
The terms might be different, but the functionality is the same.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Electrical Terms
Prevention of unexpected start-up
Energy Isolation
Safe-direction
Safe-torque-off
Safe-speed
Safe-stopping
Safe-brake control
Safe-limited-torque
Fluid Power Terms
Prevention of unexpected start-up (LOX)
Energy Isolation (Safe-exhaust)
Safe-direction (Safe-return)
Safe-torque-off (Safe-exhaust)
Safe-speed (Flow controls)
Safe-stopping (PO Checks)
Safe-brake control (Safe-return)
Safe-limited-torque (Safe-exhaust)

## Slide 5: Prevention of Unexpected Start-up is covered by Enegry Isolation or Lock-out/Tag-out
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Elimination
Fixed Guarding
Engineered Safeguards
Awareness Means, Training and Procedures (Administrative)
Personal protective equipment
Hierarchy of Protective Measures
  These measures are often combined to reduce risk to an acceptable level.
Fixed Guarding

## Slide 6
LOTO Device Considerations & Best Practices
Device Requirements
A manually operated actuator
Not be used for any other function
Located outside of hazardous areas
Easily identified and easily operated
Tamper-resistant
Lockable only in the off position
Means of energy dissapation

## Slide 7: Routine, repetitive and integral tasks are treated with risk reduction measures that use these hybrid functions.
Every mode and every task must be evaluated in order to identify all of the hazards.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Electrical Terms
Prevention of unexpected start-up
Energy Isolation
Safe-direction
Safe-torque-off
Safe-speed
Safe-stopping
Safe-brake control
Safe-limited-torque
Fluid Power Terms
Prevention of unexpected start-up (LOX)
Energy Isolation (Safe-exhaust)
Safe-direction (Safe-return)
Safe-torque-off (Safe-exhaust)
Safe-speed (Flow controls)
Safe-stopping (PO Checks)
Safe-brake control (Safe-return)
Safe-limited-torque (Safe-exhaust)

## Slide 8
Elimination
Fixed Guarding
Engineered Safeguards
Awareness Means, Training and Procedures (Administrative)
Personal protective equipment
Hierarchy of Protective Measures
This where safeguarding solutions come into consideration.
  These measures are often combined to reduce risk to an acceptable level.
Fixed Guarding
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Notes: This slides shows the recommended path for risk reduction
  Designing out the hazard is most effective
  PPE is Least effective – Note that following procedures is paramount to reducing risk, but is least effective because we do not always follow directions.
  When we do not follow directions, we are exposed to a higher level of risk – (i.e. Speeding, driving too fast for the conditions (Ice, Snow, poor visibility))
  PPE when worn appropriately does provide a significant level of protection.

## Slide 9: ISO 13849-1 – requires users to include fluid power safety as part of the safety control system.
Most metals companies ignored pneumatics and hydraulics until the ISO13849 standard included pneumatics and hydraulics as part of the safety related part of the control system.

## Slide 10: Most safety functions start with a triggering event called Safety-related stop.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 11
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
This trigger device starts the safety function action and the logic device controls the action.
Input/Triggering Device
Logic Device
Output Device
Complete Safety Function
+
+
=

## Slide 12: A Safety Function includes fluid power safety.
+
+
=
Complete Safety Function
Unfortunately, most people think that turning power off to standard valves is enough. The problem is that valves are only CatB or Cat1 devices.
+
+
=
Incomplete Safety Function
Cat4
Cat4
Cat1
Cat1
Cat4
Cat4
Cat4
Cat4
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 13
Pneumatic Safety Valve Systems
Manual Lockout Valves
Safe Exhaust
Sale Load Holding
Safe Return
Safety Expertise and Global Support
Safe Dual Pressure Select
Safe Dual Pressure Supply
Common Pneumatic Safety Solutions.

## Slide 14
Hydraulic Safety Valve Systems
Energy Isolation Lockout
Block & Bleed
Safe Return
Dual Block & Stop
Safety Expertise and Global Support
Block & Stop
Safe Dual Pressure Supply
Future
Future
Future
Common Hydraulic Safety Solutions.

## Slide 15
Functional Specifications should identify which function is to be used to reduce risk.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 16: Emergency stop requirements from NFPA79
To be used in reactions to an incident or hazard
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 17: Unfortunately, most machine do not have a safety dump valve to isolate or control fluid power energy sources.
Guess what’s missing?
The Safe-exhaust Valve!
Air Supply Line
Lock-out/Tag-out Device
Standard Pneumatic Control Valves
This is quite common in industry today. It is the same situation for hydraulic systems.
Page 55 of 56
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 18
Safe Exhaust dumps pneumatic energy to inhibit the ability to generate force and pressure.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 19
Safe return changes the direction of travel of an actuator which eliminates a potential hazard.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 20
Safe load holding stops travel of an actuator and holds a load on place which eliminates a potential hazard.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 21
Safe Exhaust dumps pneumatic energy to inhibit the ability to generate force and pressure.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Safe Pressure Select
Safe pressure select is used to switch back and forth between full pressure and a safe pressure that allows operators to interact with the machine with reduced risk of energy.

## Slide 22
Safe Design Requirements
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 23
Identify the Structure (Cat)
Determine the Reliability of the System (MTTFd)
Determine the Diagnostic Coverage of the System (DC)
Determine the Common Cause Failures of the System (CCF)
Safe Design Factors

## Slide 24
Safe Design Verification Calculations
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 25
Installation & Validation
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved

## Slide 26
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
ANSI V&V Requirements

## Slide 27
Validation is required before putting the machine/system into use.
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
ISO13849-2 Validation Requirements

## Slide 28
Session wrap-up
Confidential & Privileged C 2021 ROSS Controls All Rights Reserved
Thank you for attending today’s session. A few key points to remember:
Safety doesn’t end at the wire.
Fluid power safety is a requirement.
Fluid power safety solutions are almost always integrated with electrical input and electrical logic devices.
Don’t forget that your machine is only as safe as the weakest link. If you haven’t done anything with fluid power, your machine is probably not compliant.